## Slide 1
EXECUTIVE PRESENTATION · AIB902 · GROUP 9230 TEAM 1
Where the next EGP of maintenance should go
PMARIS asset reliability: 5,000 observation windows, six sites, twelve months
45%
of loss in the top 10% of windows
2.3x
reactive vs predictive downtime
829
high-risk windows not escalated
Prepared for the Head of Reliability & Maintenance · 11 October 2026
Notes: This deck answers one question for the Head of Reliability and Maintenance: where should the next Egyptian pound of maintenance budget go? The three numbers at the bottom are the whole story: loss is concentrated, a controllable lever doubles downtime, and the escalation flag misses most of the risk.

## Slide 2
THE ANSWER
The answer: fund four levers and widen the escalation list
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
2 / 15
1
Loss is concentrated
Top 10% of windows carry 44.7% of revenue loss. High-risk windows carry 46.7%.
2
It tracks controllable levers
Strategy, spares, crew skill and PM discipline each split downtime about 2x to 3x, all statistically real.
3
The escalation flag misses it
829 of 960 high-risk windows sit at P3/P4, carrying EGP 723M of exposure.
Notes: Lead with the answer, Pyramid style. Everything after this slide is support for these three arguments.

## Slide 3
THE HEADLINE NUMBERS
EGP 1.88B lost to 54,938 hours of downtime
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
3 / 15
1.88B
EGP revenue loss, all windows
11.0 h
mean unplanned downtime per window
19.2%
of windows high-risk (failure probability ≥ 50%)
46.7%
of revenue loss sits in those windows
Chart: 
| High-risk windows | All other windows
s | 0.46678 | 0.53322
19% of windows, 47% of the loss. The high-risk slice is small enough to target and large enough to matter.
Notes: These are the four KPIs agreed in the scope brief. Totals add overlapping 30-day windows, so compare means per window, not totals.

## Slide 4
CONCENTRATION
A tenth of the windows carry 45% of the loss
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
4 / 15
44.7%
of loss in the top 10% of windows
64.8%
in the top 20%
0.63
Gini coefficient of loss
Notes: Gini 0.63. The playbook calls this the most decision-relevant number. Effort spread evenly across the fleet is mostly spent where little is lost.

## Slide 5
LEVER 1: STRATEGY
Reactive maintenance runs 2.3x the downtime of predictive
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
5 / 15
SO WHAT
Reactive 19.0 h per window; planned strategies 8.4 to 9.5 h. 906 windows (18%) are still reactive.
Notes: Bootstrap 95% intervals. The three planned strategies overlap each other: the step that matters is leaving reactive, not choosing among the planned ones.

## Slide 6
LEVER 2: SPARE PARTS
Parts shortages run 2.9x the downtime of available stock
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
6 / 15
20.8 h
Shortage · 426 windows
13.2 h
Limited · 2,196 windows
7.2 h
Available · 2,378 windows
Notes: A clean staircase with no interval touching the next. Spares status explains 6.5% of revenue-loss variance, five times what site explains.

## Slide 7
LEVERS 1 + 2 TOGETHER
The levers compound: worst combination 26 h, best 6 h
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
7 / 15
SO WHAT
A 4.5x spread between the worst and best cell. Even with parts available, reactive runs 11.4 h against 5.9 h for predictive.
Notes: Mean downtime by strategy and spares status, with counts. Reactive plus shortage is the cell to empty first; predictive plus available is the target state.

## Slide 8
LEVER 3: CREW SKILL
Basic crews run 1.8x the downtime of expert crews
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
8 / 15
Chart: 
| Basic | Intermediate | Advanced | Expert
s | 14.7783 | 12.4176 | 9.379 | 8.006
SO WHAT
2,509 windows (50%) are worked by basic or intermediate crews. Pair them with experts on high-risk assets first.
Notes: Mean downtime by technician skill level. Basic and intermediate sit clearly above advanced and expert; intervals do not overlap.

## Slide 9
LEVER 4: PM DISCIPLINE
Downtime falls steadily as PM compliance rises: 23 h to 7 h
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
9 / 15
Chart: 
| D1 · 50% | D2 · 63% | D3 · 70% | D4 · 76% | D5 · 81% | D6 · 85% | D7 · 90% | D8 · 95% | D9 · 100% | D10 · 100%
s | 22.8331 | 17.3326 | 13.7559 | 11.5295 | 9.3642 | 8.6504 | 7.1886 | 7.1229 | 5.5762 | 6.5232
Notes: PM compliance deciles, least compliant on the left, median compliance under each bar. A dose-response shape is stronger evidence than a single split.

## Slide 10
WHAT THE LEVERS COULD BE WORTH
Upper bound: up to a quarter of downtime is in play
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
10 / 15
STRATEGY
8,621 h
if reactive windows ran at the preventive average (16% of downtime)
SPARES
5,800 h
if shortage windows ran at the available-stock average (11%)
ESTIMATED, NOT MEASURED. Treat these as the ceiling a pilot would test, not as a forecast. The two overlap where reactive windows also lack parts.
Notes: These are estimates, not measurements. They assume the association is fully causal, which it is not: reactive windows also start in worse health. That is why recommendation 6 is a pilot.

## Slide 11
D · THE ESCALATION GAP
The escalation flag misses 829 of 960 high-risk windows
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
11 / 15
Flag received by the 500 largest-loss windows
Chart: 
| P1 - Immediate | P2 - High | P3 - Planned | P4 - Monitor
s | 2 | 97 | 335 | 66
829
high-risk windows flagged only P3 or P4
EGP 723M
financial exposure sitting in that gap
Notes: Executive priority is a fixed banding of an index that correlates only 0.75 with failure probability. P1/P2 cover 26.5% of the loss in the worst 10% of windows. Most of the worst windows were filed as P3 Planned.

## Slide 12
D · THE PROPOSED RULE
Add a second trigger: FP ≥ 50% on High or Critical assets
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
12 / 15
+433
windows escalated by the rule
EGP 434M
exposure covered (60% of the gap)
134 → 567
escalated windows: check capacity
Notes: On this file the rule adds 433 windows and EGP 434M of exposure to the watched list. Escalated count goes from 134 to 567, so confirm crew capacity before switching it on.

## Slide 13
CONTEXT
What does not matter, and should not get budget on its own
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
13 / 15
Site
Real but small: explains 1.3% of loss variance. Heavy-industry sites lose about 1.5x per window, largely through the same levers.
Do not run a site-vs-site campaign
Manufacturer (OEM)
No difference on downtime, loss or failure probability (p ≥ 0.57).
No OEM switch on this evidence
Operating shift
No difference on any measure (downtime p = 0.49).
No shift restructuring
Calendar month
Flat year, no momentum between months.
Plan by condition, not calendar
Notes: Site is real but small (η² 0.013 on loss). Manufacturer (p = 0.57) and shift (p = 0.49) show nothing at all.

## Slide 14
WHAT TO DO
Seven recommendations
Source: Group_9230_Team1_PMARIS_Enterprise_Dataset.csv, 5,000 observation windows
14 / 15
1
Leave reactive maintenance
critical and high-criticality assets first
2
Fund spare-parts availability
for the classes that hit shortage
3
PM at 80%+, backlog under 14 days
the operating targets
4
Upskill basic and intermediate crews
pair with experts on high-risk work
5
Add the second escalation trigger
+433 windows, after a capacity check
6
Pilot before scaling
one site converted, one matched site as control
7
Fix the asset key in the next export
unlocks per-asset history and replacement planning
Notes: Ordered by size of effect and ease. Number 6 is what turns these associations into causal, budgetable estimates.

## Slide 15
DECISIONS NEEDED
Three decisions for this quarter
1
Approve the reactive-to-planned pilot
One site, one matched control, measured on the live dashboard
2
Approve the second escalation trigger
Subject to a capacity check for 567 escalated windows
3
Request a fixed Asset_ID in the next export
So the next review can plan replacement per asset
Analysis: 02_Analysis/analyze_pmaris.py · Dashboard: 03_Dashboard · Report: PMARIS_Reliability_Assessment.pdf
15 / 15
Notes: Close on the decisions, not a thank-you slide. The pilot is the most important: it converts the 2x associations into a causal number the budget can rest on. The live dashboard will measure it.